Arduino TPS

ATtiny84 Layout Documentation

# Schematic

# Layout

# Connections
All connections to the board are described here.

## Analog
The analog input provide access to A/D Convert 1 and 2. The pinout is

1	+5V
2	ADC1
3	ADC2
4	GND

## Input
Standard TPS input section with 4 inputs protected by 220 Ohm resistors.

1	Din.1
2	Din.2
3	Din.3
4	Din.4
5	GND

## Output
Standard TPS output section with 4 outputs parallel to the on board low current LEDs.

1	Dout.1
2	Dout.2
3	Dout.3
4	Dout.4
5	GND

## PWM
PWM Outputs. Frequency 500Hz.
1	PWM1
2	GND
3	PWM2
4	GND

## Power
Power connector to power up the TPS and to get some regulated power from the internal 5V source. (max. 100mA)
1	PS, Power savings jumper, if not closed, all LEDs will be off
2	PS
3	V+in
4	GND
5	+5V
6	GND

## Servo
There are 2 RC_Servo connections on this board.
1	PWM
2	+5V
3	GND

## RC
There are two RC PWM Inputs for standard model receivers. The Pulse should be between 1ms and 2ms. The +5V pin can be powered via the internal source when the jumper A is closed. If the internal source is not wanted remove this jumper.
1	PWM
2	+5V (
3	GND

## Switches
The switches (or additional ones in parallel) can be placed outside as well.
1	PRG
2	SEL
3	Reset
4	GND