Arduino SPS

ArduninoSPS Layout Documentation
# Schematic

# Connections
All connections to the board are described here.

## Analog
The analog input provide access to A/D Convert 1 and 2. The pinout is

1	+5V
2	ADC1
3	ADC2
4	GND

## Input
Standard TPS input section with 4 inputs protected by 220 Ohm resistors.

1	Din.1
2	Din.2
3	Din.3
4	Din.4
5	GND

## Output
Standard TPS output section with 4 outputs parallel to the on board low current LEDs.

1	Dout.1
2	Dout.2
3	Dout.3
4	Dout.4
5	GND

## PWM
PWM Outputs. Frequency 500Hz.
1	PWM1
2	GND
3	PWM2
4	GND

## Power
Power connector to power up the TPS and to get some regulated power from the internal 5V source. (max. 100mA)
1	PS, Power savings jumper, if not closed, all LEDs will be off
2	PS

1	V+in
2	GND
3	+5V
4	GND

## Servo
There are 2 RC_Servo connections on this board.
1	PWM
2	+5V
3	GND

## RC
There are two RC PWM Inputs for standard model receivers. The Pulse should be between 1ms and 2ms. The +5V pin can be powered via the internal source when the jumper A is closed. If the internal source is not wanted remove this jumper.
1	PWM
2	+5V (
3	GND

## Switches (Taster)
The switches (or additional ones in parallel) can be placed outside as well.
1	PRG
2	SEL
3	Reset
4	GND

## Serial
With the serial connector you can interact (or debug) with the mcu over a serial protocol. Mainly in TPS applications use to load new programs into the unit.
1	TX
2	RX
3	GND

## Display
The display connector is used for a TM1637 like 7 segment display.
1	CLK
2	DATA
3	+5V
4	GND

## ISP
The isp connector is used for a standart isp programmer.
1	MISO
2	+5V
3	SCK
4	MOSI
5	RESET
6	GND

# BOM
Pos	Anzahl	Name	Wert	Gehäuse
1	2	C1,C2	100nF	2,54x5,08_RM2,54
2	2	C3,C4	1µF	C_RM5,08
3	2	C7,C8	22pF	3X7R2,54
4	1	D1	Dout.1	LED_3MM_GELB
5	1	D2	Dout.2	LED_3MM_GELB
6	1	D3	Dout.3	LED_3MM_GELB
7	1	D4	Dout.4	LED_3MM_GELB
8	1	D5	Grün Power	LED_3MM_GRÜN
9	1	D6	1N4148	DO35
10	1	D7	1	LED_3MM_GELB
11	1	D8	2	LED_3MM_GELB
12	1	IC1	ATmega328P-PU	DIL28_WB7,62_P2,54
13	1	K1	Servo1	Stiftleiste_1x03_G_2,54
14	1	K2	Servo2	Stiftleiste_1x03_G_2,54
15	1	K3	RC1	Stiftleiste_1x03_G_2,54
16	1	K4	RC2	Stiftleiste_1x03_G_2,54
17	1	K5	Analog	Stiftleiste_1x04_G_2,54
18	1	K6	Output	Stiftleiste_1x05_G_2,54
19	1	K7	Input	Stiftleiste_1x05_G_2,54
20	1	K8	Taster	Stiftleiste_1x04_G_2,54
21	1	K9	Power	Stiftleiste_1x04_G_2,54
22	1	K10	ISP	Stiftleiste_2x03_G_2,54
23	1	K11	A2	Stiftleiste_1x02_G_2,54
24	1	K12	A1	Stiftleiste_1x02_G_2,54
25	1	K13	PWM	Stiftleiste_1x04_G_2,54
26	1	K14	Serial	Stiftleiste_1x03_G_2,54
27	1	K15	Display	Stiftleiste_1x04_G_2,54
28	1	K16	PS	Stiftleiste_1x02_G_2,54
29	1	K17	Aux	Stiftleiste_1x02_G_2,54
30	1	K18	microUSB	JAE_DX4R005H91
31	1	Q1	16MHz	HC49/US
32	6	R1,R2,R3,R4,R11,R12	1,4K	0207_MET
33	1	R5	1,4K	0204_MET
34	1	R6	10k	0207_MET
35	4	R7,R8,R9,R10	220	0207_MET
36	1	S1	SEL	TASTER_KURZHUB
37	1	S2	PRG	TASTER_KURZHUB
38	1	S3	Reset	TASTER_KURZHUB
39	1	X1	MCP1703-5002	SOT223

If the LEDs are LowCurrent LEDs with 2mA, so the resistors are 1k4. If you are using normal LEDs with 20mA the value of the resistors is 150Ohm.